## Slide 1
DSv3 MoE Training Performance
TPU v7x · 4×8×8 · 512 devices
BS=1024 · EP=8 · FSDP=64
Roofline analysis · ICI bottleneck breakdown · Engineering roadmap

## Slide 2
v7x Hardware: What We're Working With
MXU (bf16)
2,307
TFLOP/s per chip
HBM BW
7,373
GB/s per chip
ICI (cross-chip)
~90
GB/s per link
ICI (same chip)
600
GB/s intra-chip
HBM capacity
95
GB per chip
2 cores (JAX devices) per chip → per-device: 1,153 TFLOP/s · 3,686 GB/s HBM · 32 GB VMEM
Roofline: when is an op compute-bound vs memory-bound?
# Operational intensity (OI) = FLOPs / bytes_accessed # Ridge point = peak_compute / peak_memory_bw peak_flops_bf16 = 1153e12 # FLOP/s per device peak_hbm_bw = 3686e9 # bytes/s per device ridge_point = peak_flops_bf16 / peak_hbm_bw # OI threshold # → 1153e12 / 3686e9 = 313 FLOP/byte # If OI > 313: compute-bound (MXU is the bottleneck) # If OI < 313: memory-bound (HBM bandwidth is the bottleneck)
Ridge point
313 FLOP/byte
An op needs to do 313 FLOPs per byte read/written to saturate the MXU. Below that — you're just waiting on HBM.

## Slide 3
Expert FFN: Is It Compute-Bound?
Operational intensity of the core matmuls — before any communication
# Per-expert forward pass (one of 32 local experts) # tpe = 1,536 tokens D = 7,168 F = 2,048 h_gate = tok_e @ W_gate.T # (tpe, D) × (D, F) → (tpe, F) h_up = tok_e @ W_up.T # (tpe, D) × (D, F) → (tpe, F) act = silu(h_gate) * h_up out_e = act @ W_out.T # (tpe, F) × (F, D) → (tpe, D) # FLOPs (one expert, forward): flops_w1 = 2 * tpe * D * F # = 2 × 1536 × 7168 × 2048 = 45 GFLOP flops_w2 = 2 * tpe * F * D # = 2 × 1536 × 2048 × 7168 = 45 GFLOP (same) # ×2 because gate+up share the same D→F projection total_fwd = 2 * (flops_w1 + flops_w2) = 181 GFLOP per expert # Bytes read (weights, bf16, once per expert): bytes_W_gate = D * F * 2 = 29.4 MB bytes_W_up = D * F * 2 = 29.4 MB bytes_W_out = F * D * 2 = 29.4 MB total_bytes = 88 MB (plus 88 MB tokens + activations)
OI — expert FFN
181 GFLOP / 176 MB = 1,028 FLOP/byte
Ridge point: 313 FLOP/byte → 3× above ridge
✓ Expert FFN is compute-bound (MXU is the bottleneck for FFN)
But: 32 experts × 15 ms = ?
Compute per device per MoE layer:
17,391 GFLOP (4× fwd) @ 1,153 TFLOP/s
= 15 ms per MoE layer
Problem: ICI takes 28 ms. Compute is not the limit.

## Slide 4
Token Flow: From GBS to tpe
How 4M training tokens get distributed to 32 local experts per device
# Global config GBS = 1024 # sequences in this batch seqlen = 4096 # tokens per sequence n_total_tokens = GBS * seqlen # 4,194,304 # Device count EP, FSDP = 8, 64 n_devices = EP * FSDP # 512 (256 chips × 2 cores) # Per-device token shard (act_spec = P(('ep','fsdp'), None)) T_local = n_total_tokens // n_devices # 8,192 tokens # Inside shard_map: EP all_gather reconstructs FSDP-local view T_fsdp = T_local * EP # 65,536 tokens # All 8 EP ranks within a FSDP group see the same 65,536 tokens # Routing (DSv3: 256 routed experts, top-6) K, E = 6, 256 E_local = E // EP # 32 experts per EP rank token_expert_pairs = T_fsdp * K # 393,216 pairs_for_this_rank = token_expert_pairs // EP # 49,152 tpe = pairs_for_this_rank // E_local # 1,536 (avg) # + 2 shared experts (replicated, no A2A needed)
Token pipeline
4,194,304 tokens
global batch
↓
8,192 tokens
T_local / device
↓
65,536 tokens
T_fsdp after EP gather
↓
49,152 pairs
for this rank's 32 experts
↓
1,536 avg
tokens per expert (tpe)

## Slide 5
EP Topology: Not All ICI Is Equal
EP=8 spans 4 chips × 2 cores. Same-chip core pairs communicate at 600 GB/s.
Physical layout: EP=8 on 4 chips, 2 cores each
Chip 0
EP rank 0
core 0
EP rank 1
core 1
Chip 1
EP rank 2
core 0
EP rank 3
core 1
Chip 2
EP rank 4
core 0
EP rank 5
core 1
Chip 3
EP rank 6
core 0
EP rank 7
core 1
⟺
⟺
⟺
⟺
600 GB/s (intra-chip)
→
→
→
~90 GB/s per ICI link (cross-chip)
A2A traffic per device per MoE layer (forward token send, K=6, T_fsdp=65,536)
Destination
Pairs
Volume
Bandwidth
Time
Local EP rank (own)
49,152
0 bytes
—
0 ms
Co-chip EP rank (×1)
49,152
703 MB
600 GB/s
~1 ms
Cross-chip EP (×6)
49,152 ea
703 MB ea
~90 GB/s
~8 ms
Total ICI (slow path)
295,000
4.2 GB
150 GB/s agg
~28 ms

## Slide 6
The Bottleneck: ICI, Not MXU
Even at peak MXU efficiency, A2A ICI is 2× slower than expert FFN compute
# Per MoE layer, per device # --- Compute --- flops_per_layer = 32 * 1536 * (2*7168*4096 + 2*2048*7168) * 4 # fwd+bwd+recompute # = 17,391 GFLOP compute_time_ms = 17_391 / 1_153_000 * 1000 # @ 1153 TFLOP/s # = 15 ms # --- ICI (cross-chip only; local + co-chip are free) --- tokens_for_remote_experts = T_fsdp * K * 6/8 # 6 cross-chip EP ranks # = 65536 * 6 * 0.75 = 295,000 token slots bytes_one_direction = 295_000 * 7168 * 2 # BF16 # = 4.2 GB ici_time_ms = 4.2e9 / 150e9 * 1000 # 150 GB/s aggregate # = 28 ms # 4 transfers on critical path (fwd send, fwd recv, bwd send, bwd recv) # With perfect layer-to-layer pipelining → effective ~56 ms / layer # Without pipelining → 4 × 28 = 112 ms / layer # ICI / Compute ratio = 28 ms / 15 ms = 1.87× # Even MXU at 100% can't hide the ICI cost without pipelining.
Per-layer time budget
Compute (MXU)
15 ms
ICI one direction
28 ms
ICI 4× (no pipe)
112 ms
ICI (pipelined)
56 ms
Key insight: SC offload frees MXU from scatter/gather, but MXU is not the bottleneck — ICI is. The real gain is from A2A DMA pipelining across layers.

## Slide 7
A2A Pipelining: The Critical Optimisation
Overlap ICI of layer N with expert FFN compute of layer N−1
# Naive (sequential): every layer stalls on ICI # ───────────────────────────────────────────────── for layer in moe_layers: tokens = a2a_send(sorted_tokens) # 28 ms — STALL out = expert_ffn(tokens) # 15 ms result = a2a_recv(out) # 28 ms — STALL # per layer: 28+15+28 = 71 ms → 58 layers = 4.1 s # Pipelined (DMA runs concurrently with compute): # ───────────────────────────────────────────────── issue_a2a(layer[0].tokens) # start layer 0 ICI for i, layer in enumerate(moe_layers): wait_a2a(layer[i].tokens) # wait for this layer's tokens if i+1 < len(moe_layers): issue_a2a(layer[i+1].tokens) # prefetch next layer's tokens out = expert_ffn(layer[i].tokens) # compute overlaps with ^ ICI issue_a2a(layer[i].out) # send results back wait_a2a(layer[i-1].out) # collect previous results # per layer: max(28, 15) = 28 ms → 58 layers = 1.6 s # (bwd further overlaps: effective ~56 ms fwd+bwd / layer)
ICI / Compute timeline
Layer 0
ICI↑
FFN
ICI↓
Layer 1
ICI↑
FFN
ICI↓
Layer 2
ICI↑
FFN
ICI↓
ICI↑ and ICI↓ of adjacent layers overlap → 28 ms critical path

## Slide 8
Step Time Estimate: Full Optimised Stack
BS=1024 · EP=8 · FSDP=64 · 58 MoE + 61 MLA + 3 dense · fwd+bwd+recompute
Per-step time budget (with perfect A2A pipeline + FSDP overlap)
58 MoE layers (ICI-bound, ~56 ms/layer pipelined)
3.2 s
61 MLA attention layers (compute-bound)
0.13 s
3 dense MLP layers
0.02 s
FSDP weight all-gather (overlapped w/ compute)
~0
TOTAL
~3.4 s
Scenarios
Scenario
Step time
TPS/chip
vs v10
Optimistic (perfect pipeline)
3.4 s
~4,800
+10.3×
Realistic (60% efficiency)
5.5 s
~2,960
+6.4×
Conservative (40% efficiency)
8 s
~2,040
+4.4×
v10 ragged_dot (baseline)
~35 s
465
1.0×

## Slide 9
Why A2A Eliminates the EP All-Reduce
Current streaming_bwd uses psum(d_tok, 'ep') per layer — the most expensive collective
# Current (streaming_bwd v1): EP all-reduce # ───────────────────────────────────────── def _streaming_bwd_fn(g_l, fx_l, fw_l, fi_l, w0_l, w1_l, wout_l): # EP all_gather to see all T/FSDP tokens fx_full = lax.all_gather(fx_l, 'ep') # ICI # ... expert FFN backward ... d_tok_partial = per_expert_backward() # ALL-REDUCE: every EP rank needs to sum # contributions from ALL other EP ranks d_tok_full = lax.psum(d_tok_partial, 'ep') # ^^ 65536 × 7168 × 4B × 2 (all-reduce) # = 3.76 GB per layer per device # = 3.76 / 150 GB/s = 25 ms per layer # = 25 ms × 58 layers = 1.45 s extra # Plus: global sync point — no overlap
# Pallas A2A: point-to-point DMA, no psum # ───────────────────────────────────────── # Forward: # sort tokens → DMA sorted_tokens to # the 7 EP peers that own their experts # → each expert rank receives exactly # the tokens it needs. No broadcast. # Backward: # each expert rank computes d_tok_e # DMA d_tok back to token-owner ranks # token owners scatter-add contributions # → no all-reduce needed at all # ICI traffic comparison per layer: # all-reduce: 3.76 GB (blocking) # A2A send: 4.2 GB (async DMA) # A2A recv: 4.2 GB (async DMA) # Total A2A = more bytes but ASYNC → # overlaps with compute of next layer.
Current EP psum: 58 × 25 ms = 1.45 s (blocking)
Global sync every layer — cannot pipeline
A2A DMA: async, pipelines with FFN compute
No blocking collective — ICI hidden in compute shadow

## Slide 10
Engineering Roadmap
Four work items to go from current streaming_bwd to full Pallas A2A kernel
1
Pallas Forward Kernel (Expert FFN A2A)
NOT STARTED
• Replace shard_map+psum EP forward with Pallas A2A
• sort tokens → DMA send → per-expert FFN → DMA recv → scatter-add
• SC-offloaded indexed gather for token packing (sc_gather_rows)
• Validate: loss matches jax baseline at full scale
Impact: Eliminates EP all_gather in fwd (65536×7168 per layer)
2
Pallas Backward Kernel (Expert FFN Backward + A2A)
IN PROGRESS
• streaming_bwd v1/v2: JAX backward running, SC Get fix in v73
• Replace EP psum(d_tok) with reverse A2A DMA (no all-reduce)
• FSDP weight all-gather double-buffered across E_local experts
• Validate: loss curve 86.703→86.561 matching v60 baseline
Impact: Eliminates EP psum (1.45 s/step) — biggest single win
3
Layer-to-Layer A2A Pipeline
NOT STARTED
• Issue DMA for layer n+1 tokens while computing layer n FFN
• Double-buffer: two A2A slots (inflight + being processed)
• Requires ICI DMA API that returns before transfer completes
• Target: ICI fully hidden behind compute (56 ms → 15 ms/layer)
Impact: Closes compute/ICI gap: ~3.4 s vs ~5.5 s step time
4
FSDP All-Gather Overlap (Attention + Dense)
PARTIAL
• Async collective flags already in LIBTPU_INIT_ARGS (--xla_enable_async_all_gather)
• Per-layer all_gather issued before layer compute, reduce-scatter after
• Attention: 4 weight projections × 205 MB per layer × 61 layers = 50 GB
• Currently: XLA handles via async collectives; Pallas gives explicit control
Impact: Hides 50 GB attention + 328 GB MoE weight ICI in compute shadow

## Slide 11
Summary: Where Performance Comes From
v7x ridge point is 313 FLOP/byte
Expert FFN OI ≈ 1,028 — solidly compute-bound in isolation.
Expert FFN is NOT the bottleneck
At 1,536 tpe, each expert takes 15 ms compute vs 28 ms ICI. ICI wins.
EP A2A topology matters
1/8 traffic is local (free). 1/8 is 600 GB/s co-chip (near-free). 6/8 is cross-chip at ~90 GB/s.
EP all-reduce is the single biggest waste
Current psum: 1.45 s/step, blocking. A2A DMA: async, pipelines with compute.
A2A layer pipelining is the key lever
Perfect pipelining → 3.4 s step. Realistic → 5.5 s. Either is 6–10× over v10 (465 TPS/chip).
SC offload helps but is not critical
Frees MXU from scatter/gather, but MXU is already not the bottleneck.
Realistic target with full Pallas A2A + pipelining: ~5.5 s/step · ~2,960 TPS/chip · 6× over v10